Brainpop Video– Recycling

Dear Tim and Moby,

How does recycling work?

Sabina

Recycling means that we take something like this newspaper from last Sunday, and process (处理) it so it can be used again.  All sorts of things can be recycled; paper, plastic, aluminum cans, batteries, and even motor oil.  Sorting (分类)is the first step in recycling.  Some cities require higher levels of sorting, like making sure different kinds of paper are separate.  But the most common requirement is to place paper products in one bin; sturdy containers – like glass and plastic bottles and metal cans – in another; and regular trash in a third bin.  Then, you either drop off your recyclables or put them out to be collected.

Newspapers are taken to a paper mill (纸厂).  At the mill, paper goes through a chemical wash (化学洗涤) to separate the ink from paper.  A slusher turns the old paper into a mushy mix of paper fiber called pulp (纸浆).  Detergent (soap) dissolves (溶解) the ink and carries it away.  Screens (筛子) remove contaminants like bits of tape or dirt.  The pulp that’s left gets bleached (whitened) and mixed with additional pulp from wood chips to strengthen it.  The pulp is poured onto a moving screen that lets the moisture (water) out.  Once it’s hardened, the paper is fed through steam (蒸汽) heated rollers that flatten it into a continuous sheet of paper.  Tomorrow’s newspaper can be printed on that same paper, and the recycling loop is complete.

Yeah, that soda can is eventually going to a recycling plant, too – an aluminum recycling plant... obviously.  First, the aluminum gets shredded (cut) into small pieces.  Then the pieces are all melted (熔化) into a huge furnace to make molten, or liquefied, aluminum.  Lastly, they’re shaped into metal casts called ingots that can be melted down later and used for making new aluminum products.

Well, plastics are a little more complicated.  That’s because there are many different types of plastic, and they can’t be mixed with other types.  Most plastics have a little recycle sign on them with a number and a special code.  That’s the resin identification code, and each one stands for a different type of plastic.  So, before they can be recycled, plastics need to be very carefully sorted.  Actually, many communities only recycle a few types of plastic because it’s too expensive to recycle every kind.  So make sure you check with your local recycling program to see what can and can’t be recycled.  Most things with a 1, 2, or 3 identification code usually can be recycled – things like water and soda bottles, grocery bags, milk and juice cartons, and detergent (soap) bottles.

Well, yeah, it does take some work to recycle, but recycling is better for us and for the earth.  Recycling reduces pollution, energy, and the use of raw materials; it creates jobs; and it reduces the need for landfills.